## Slide 1: THESIS PROPOSAL
Satellite Ground Station
for
CubeSats and LEO satellites

## Slide 2: CONTENTS
Introduction
Literature review
Method and expected outcomes
Timeline
Budget plan

## Slide 3: Introduction
A kick-start in space engineering
There are considerable “herd” of satellites up there!
Notes: Khoa học vũ trụ và kỹ thuật hàng không hiện đại đang gặt hái rất nhiều thành công. Trong quá trình thương mại hóa không gian, sự tham gia của các công ty tư nhân vào lĩnh vực này khiến cho công nghệ chế tạo phát triển vượt bậc kéo theo rất nhiều chi phí giảm đi đáng kể so với nhiều thập kỷ trước, đặc biệt là về kỹ thuật chế tạo vệ tinh. Số lượng các vệ tinh này đang gia tăng rất nhanh, nhất là Cubesat – một loại vệ tinh nhỏ có kích thước đơn vị 10cmx10cmx10cm thực hiện được nhiều nhiệm vụ quan trọng

## Slide 4
“SpaceX successfully launches first 60 satellites in massive Starlink internet constellation“ – The Verge
NextBigFuture.com

## Slide 7: Introduction
A kick-start in space engineering
There are considerable “herd” of satellites up there!
Links must be established -> How?
Notes: Trạm mặt đất là hệ thống dùng để giao tiếp với các vệ tinh hoặc thiết bị bay [2]. Việc thiết kế các trạm này sao cho phù hợp với số lượng đông đúc các vệ tinh mà vẫn đảm bảo tính ổn đinh, độ linh hoạt với nhiều vệ tinh và chi phí thấp là vô cùng cần thiết. Từ các lợi thế này, có thể nhân rộng để khai thác cho mục đích thương mại.

## Slide 8
SATELLITE GROUND STATION
Notes: Trạm mặt đất là hệ thống dùng để giao tiếp với các vệ tinh hoặc thiết bị bay [2]. Việc thiết kế các trạm này sao cho phù hợp với số lượng đông đúc các vệ tinh mà vẫn đảm bảo tính ổn đinh, độ linh hoạt với nhiều vệ tinh và chi phí thấp là vô cùng cần thiết. Từ các lợi thế này, có thể nhân rộng để khai thác cho mục đích thương mại.

## Slide 9: Literature review
Ground station functionality
------------------------------------- Tracking mechanism

## Slide 10
S. P. A. N. Erika Pittella, "Design of an Antenna System for CubeSat Satellites," in 2nd IAA Conference on University Satellites Missions and CubeSat Winter Workshop, 2013.

## Slide 11
Notes: You may be familiar with this guy

## Slide 12
Notes: Now, there is another reference frame: of Azimuth and Elevation

## Slide 13: Literature review
Ground station functionality
------------------------------- Tracking mechanism
------------------------------- Radio frequency transceiver

## Slide 14: Literature review
Ground station functionality
------------------------------- Tracking mechanism
------------------------------- Radio frequency transceiver

## Slide 16: Literature review
Ground station functionality
------------------------------- Tracking mechanism
------------------------------- Radio frequency transceiver
------------------------------- Signal processing

## Slide 17: Literature review
Ground station functionality
Vinasat 1,2
--------------------------- They are geostationary satellites
--------------------------- They do have ground station

## Slide 18
Ground station at Cát Quế, Hoài Đức – Hà Nội
vov.vn

## Slide 19: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon

## Slide 20: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
------------------------ Built by VNSC, in the help of Japan

## Slide 21: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
------------------------ Built by VNSC, in the help of Japan
------------------------ Manufactured in Japan

## Slide 22: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
------------------------ Built by VNSC, in the help of Japan
------------------------ Manufactured in Japan
------------------------ Launched by Japan

## Slide 23: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
------------------------ Built by VNSC, in the help of Japan
------------------------ Manufactured in Japan
------------------------ Launched by Japan
------------------------ Observed by JAXA - Japan

## Slide 24: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
------------------------ Built by VNSC, in the help of Japan
------------------------ Manufactured in Japan
------------------------ Launched by Japan
------------------------ Observed by JAXA - Japan
------------------------ Vietnamese proudness !??
Notes: JAXA | Japan Aerospace Exploration Agency

## Slide 25: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon

## Slide 26: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions

## Slide 27: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
------------------------ CubeSatsShop, ISIS Space…

## Slide 28: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
------------------------ CubeSatsShop, ISIS …
------------------------ Full options: 86.500 EURO

## Slide 29
Full options kit of ISIS
www.isisspace.nl
Notes: ISIS - Innovative Solutions In Space, - Netherland
Motorenweg 23, 2623 CR Delft

## Slide 30: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
Limited payload

## Slide 31: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
Limited payload
------------------------ 2 yagis and 1 parabolic antenna
------------------------ Investigation for RF is significant

## Slide 32
blogs.aalto.fi

## Slide 33
eusoc.upm.es

## Slide 34
CubeSatShop.com

## Slide 35: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
Limited payload

## Slide 36: Literature review
Ground station functionality
Vinasat 1,2
Micro Dragon
Pico Dragon and Nano Dragon
Commercial solutions
Limited payload
For CubeSat
Ground Station
Low cost
Universal
antennas
mounting

## Slide 37
For CubeSat
Ground Station
Low cost
Universal
antennas
mounting

## Slide 38: Novelties
Functionality for CubeSats/Nanosats
Universal antennas mounting and multiple frequencies hopping
Low cost, estimated by budget plan

## Slide 39: Methods
Literature research on space engineering, spacecraft dynamic and satellite communicating

## Slide 40: Methods
Literature research on space engineering, spacecraft dynamic and satellite communicating
------------------------ Keplerian elements
------------------------ Satellites ADCS
------------------------ Radio link and communication

## Slide 41
adcsforbeginners.wordpress.com
Keplerian elements

## Slide 42: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software

## Slide 43: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
------------------------ Hardware design and construct
------------------------ Host computer controlled
------------------------ Software calculating position
------------------------ Firmware in sub-system

## Slide 44
Rotary system

## Slide 45
In construction

## Slide 46
In construction and me!

## Slide 47: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
RF design

## Slide 48: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
RF design
------------------------ Antennas design and constructing
------------------------ Filters, amplifier
------------------------ Signal processing software

## Slide 51: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
RF design
Evaluate the accuracy

## Slide 52: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
RF design
Evaluate the accuracy
------------------------ Evaluate the rotary tolerance
------------------------ Evaluate the RF system

## Slide 54
Bubble meter
uk.rs-online.com

## Slide 55: Method
Literature research on space engineering, spacecraft dynamic and satellite communicating
Designing and building rotary system with computer interfaces software
RF design
Evaluate the accuracy
Report and finalizing

## Slide 56
General system diagram

## Slide 57: Expected outcomes
 | Description | Criteria/Deliverable
Hardware | Two axes rotational system with universal mount for satellite tracking purpose and its controller working in both manual and automatic mode | . Mechanical frame . Two axes with accuracy ±5 degrees and speed of 1 degree/second in minimum . Have ability to be mounted: + Parabolic antenna: 3m diameter, 20kg + Two Yagi antennas: 0.5m x 0.5m x 2m, 5kg . Wide range working frequency based on capacity of the used SDR (USRP B210: 70Mhz to 6Ghz)
Software | A program interfacing with SDR for frequency switching and signal processing | . Software to control the azimuth and elevation axis manually by tuning gauge in user interface. . Software has availability to track the LEO satellite automatically. . Software can interface with SDR, tuning frequencies. . Software can receive the beacon signal and un-decoded downlink data.
Paper |  | Paper about Satellite ground station using SDR.

## Slide 58: Timeline
1-year project
Tasks will be assigned to team members in detail

## Slide 59: Timeline
Step | From | To | Duration | Jobs | Detail
1 | October 21st , 2018 | December 1st , 2018 | 1.5 months | Literature review and planning for the structure | Statistic the need of SGS
 |  |  |  |  | Satellite communicating
 |  |  |  |  | Dynamic of spacecraft
 |  |  |  |  | Mechanism of structure
2 | December 6th, 2018 | April 29th, 2019 | 5 months | Building rotary system | Detail design of mechanical structure
 |  |  |  |  | Construct the structure
 |  |  |  |  | Design electrical system
 |  |  |  |  | Software programing and graphic user interface

## Slide 60: Timeline
Step | From | To | Duration | Jobs | Detail
3 | February 1st, 2019 | May 29th, 2019 | 4 months | SDR research | Interfacing with SDR to turning frequency and signal processing
 |  |  |  |  | Construct antenna feed line and switching
 |  |  |  |  | Combine the SDR part to software at step 2
4 | June 1st , 2019 | August 15th, 2019 | 2.5 months | Evaluate the model | Evaluate the accuracy of orienting
 |  |  |  |  | Perform the tracking ability on broadcast signal of satellite
5 | August 20th, 2019 | October 1st, 2019 | 1.5 months | Complete the report and papers | Writing report
 |  |  |  |  | Paper for rotary part
 |  |  |  |  | Paper for SDR part

## Slide 61: Budget plan
107.000.000 VND - labor cost included
21 times lower than typical commercial version

## Slide 62: Budget plan
Item | Estimated cost | Request funding | Note
Aluminum frame and accessories | 6.000.000 VND | 6.000.000 VND | This is used for constructing the frame on ground station. Which is popular in industry because of its convenience in high load strength and assembling easily
Aluminum sheet and billet | 3.000.000 VND | 3.000.000 VND | Aluminum sheet (6061 type) is used to fabricating parts of rotating structure.
Motor drive system (with controllers) | 8.000.000 VND | 8.000.000 VND | Harmonic and worm gear drive are for capacity of high load and precision.
Main controller | 2.000.000 VND | 2.000.000 VND | Proposed to use the MSP432 launchpad or similar device which can provide real time calculation.

## Slide 63
PCB manufacturing and circuit components (power ICs, transistor, resistor…) | 3.000.000 VND | 3.000.000 VND | Some PCB would be made for attaching the main controller to connecting many peripherals.
Wire and connector for cable management | 1.000.000 VND | 1.000.000 VND | 
Parabolic antenna and Yagi antenna | 10.000.000 VND | 10.000.000 VND | Based on market research, one 3m parabolic antenna (around 30dBi) has price of nearly $300 and one Yagi is about $50
LNA filter, SMA, RF accessories | 2.000.000 VND | 2.000.000 VND | 
Manufacturing | 10.000.000 VND |  | Will be proposed to use CNC machines in GPEM labs
Labor | 60.000.000 VND |  | Brief estimate based on general working hours of team members
Misc (screws, nuts, spray, pulley, bearing, wheels, drills…) | 2.000.000 VND | 2.000.000 VND | Already paid in advance
Total | 107.000.000 VND | 37.000.000 VND | We already paid 19.000.000 VND in advance to start working seriously on this project.
Budget plan

## Slide 64
Manufacturing | 10.000.000 VND |  | Will be proposed to use CNC machines in GPEM labs
Labor | 60.000.000 VND |  | Brief estimate based on general working hours of team members
Misc (screws, nuts, spray, pulley, bearing, wheels, drills…) | 2.000.000 VND | 2.000.000 VND | Already paid in advance
Total | 107.000.000 VND | 37.000.000 VND | We already paid 19.000.000 VND in advance to start working seriously on this project.
Manufacturing | 10.000.000 VND |  | Will be proposed to use CNC machines in GPEM labs
Labor | 60.000.000 VND |  | Brief estimate based on general working hours of team members
Misc (screws, nuts, spray, pulley, bearing, wheels, drills…) | 2.000.000 VND | 2.000.000 VND | Already paid in advance
Total | 107.000.000 VND | 37.000.000 VND | 
Budget plan

## Slide 65
Questions ?